RISC-V 2-trins afkodning
Slides fra COD – maltrakteret af Finn Schiermer Andersen

---
The Main Control Unit
Decoding RISC-V
Instruction layouts
Chapter 4 — The Processor —
[Speaker Notes: Morgan Kaufmann Publishers 4 December 2022 Chapter 4 — The Processor]

---
Datapath With Control
Datapath With Control
[Speaker Notes: Morgan Kaufmann Publishers 4 December 2022 Chapter 4 — The Processor]

---
ALU Control
ALU Control
ALU used for
  - Load/Store: F = add
  - Branch: F = subtract
  - R-type: F depends on opcode
ALU control	Function
0000	AND
0001	OR
0010	add
0110	subtract
§4.4 A Simple Implementation Scheme
[Speaker Notes: Morgan Kaufmann Publishers 4 December 2022 Chapter 4 — The Processor]

---
ALU Control
Assume 2-bit ALUOp derived from opcode
  - Combinational logic derives ALU control
opcode	ALUOp	Operation	Opcode field	ALU function	ALU control
ld	00	load register	XXXXXXXXXXX	add	0010
sd	00	store register	XXXXXXXXXXX	add	0010
beq	01	branch on equal	XXXXXXXXXXX	subtract	0110
R-type	10	add	100000	add	0010
		subtract	100010	subtract	0110
		AND	100100	AND	0000
		OR	100101	OR	0001
[Speaker Notes: Morgan Kaufmann Publishers 4 December 2022 Chapter 4 — The Processor]

---
The ALU Control Unit
- Control signals derived from
  - ALUOp
  - Funct7
  - Funct3
[Speaker Notes: Morgan Kaufmann Publishers 4 December 2022 Chapter 4 — The Processor]

---
Main Control Unit
Figure 4.26 The control function for the simple single-cycle implementation is completely
specified by this truth table. The top seven rows of the table gives the combinations of input signals
that correspond to the four instruction classes, one per column, that determine the control output settings.
The bottom portion of the table gives the outputs for each of the four opcodes. Thus, the output RegWrite
is asserted for two different combinations of the inputs. If we consider only the four opcodes shown in
this table, then we can simplify the truth table by using don’t cares in the input portion. For example, we
can detect an R-format instruction with the expression Op4 ∙ Op5, since this is sufficient to distinguish the
R-format instructions from lw, sw, and beq. We do not take advantage of this simplification, since the rest
of the RISC-V opcodes are used in a full implementation.
Copyright © 2021 Elsevier Inc. All rights reserved.